| OHS FORM 05: SAFE WORK METHOD STATEMENT (SWMS) –02 EXCAVATOR OPERATION CUT/FILL/TRENCHING |
| --- |
| Company name: Collective Civil Pty Ltd ABN: 53 097 428 003 | This SWMS has been developed and authorised by: |
|  | Name | Kiri Krishnapillai |
|  | Position | Project Manager | Date | 06/09/10 |
|  | Signature |  | Phone |  |
|  |  |  | Mobile | 0458 180 902 |
| DESCRIPTION OF WORK ACTIVITY: EXCAVATOR OPERATION CUT/FILL/TRENCHING |
| Trades involved with undertaking this work activity: |
| This SWMS is submitted to (principal contractor): |
| COMPANY: EWG |
| CONTACT NAME: Siva Sivakumar | CONTACT NAME: |
| SITE ADDRESS: Station Road, AUBURN | PROJECT DESCRIPTION: Road & Drainage Works |
| This SWMS was reviewed by (principal contractor): |
| NAME: | POSITION: Superintendent |
| SIGNATURE: | DATE: |
| PHONE NUMBER: | MOBILE NUMBER: |
| Person responsible for supervising and implementing, on the contractor’s behalf, the OHS controls associated with each step of this work activity. |
| NAME: Troy Hanepen POSITION: |
| SIGNATURE: | DATE: 06/09/10 |
| PHONE NUMBER: | MOBILE NUMBER: 0412 992 957 |
| List plant, equipment and tools to be used | List hazardous substances to be used or handled | MSDS available? (Tick) | List PPE to be used | (Tick) | List hazards to consider | (Tick) |
| eg Electric generator | eg Unleaded petrol |  | Hard hat |  | Fall from ladder |  |
|  |  |  | Safety boots |  | Fall from heights |  |
|  |  |  | High-visy clothing |  | Fall from scaffold |  |
|  |  |  | Gloves |  | Contact with electricity |  |
|  |  |  | Hearing protection |  | Falling objects |  |
|  |  |  | Safety glasses |  | Collapse |  |
|  |  |  | UV cream |  | Slip, trips and falls |  |
|  |  |  | Dust masks |  | Manual handing |  |
|  |  |  | 30+ sunscreen |  | Exposure to noise |  |
|  |  |  | Other (specify): |  | Struck by moving plant |  |
|  |  |  |  |  | Inhalation of dust or fumes |  |
|  |  |  |  |  | Cuts |  |
|  |  |  |  |  | Other (specify): |  |
| RISK TABLE How likely is it to be serious? NOTE: If a hazard is rated 1, 2 or 3, take action immediately. What damage could it cause? Very likely (could happen anytime) Likely (could happen sometimes) Unlikely (could happen, but only rarely) Very unlikely (could happen, but probably never will) Death or permanent disability 1 1 2 3 Long term illness or serious injury 1 2 3 4 Medical attention and several days off work 2 3 4 5 First aid needed 3 4 5 6 | How to complete the following form List the step-by-step sequence of tasks required to carry out a work activity from start to finish. List the potential hazards associated with each step, and the related OHS risks. Using the risk table, rate the identified risks. List what controls you will implement to reduce the risks to the lowest possible level. Rate the level of risk once those controls have been implemented (must be 4-6 before you can start work). List the names or positions of the persons responsible for ensuring that the controls are implemented. A separate SWMS is required for each work activity. |

| STEP | Activity step Break the activity down into steps. List the steps in this column. | Hazards Identification Identify any potential hazards associated with each step – and any related risks. Detail the hazards and risks in this column, and enter the risk rating in the next column. | Initial risk rating (1-6) | Controls Implemented Decide what controls to use to eliminate or minimise the risks. Detail the controls in this column, and enter the revised risk rating in the next column. Note: If the risk rating is still 1-3, do not begin work. | Revised risk rating (1-6) | Person responsible |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Pre check machinery/ site conditions | Slips and falls – medium Oil and grease spillage – medium Altered site conditions/new hazards | 2 | 3 point contact to enter/exit machine Clean up spills/ spill kit in machine Daily inspection of site by MH prior to commencement of work | 6 | operator |
| 2 | Track excavator/ slew excavator | Personnel struck/crushed by excavator or attachments Striking obstacles/ overhead services | 1 | Ensure correct operation of movement alarms on excavator, high vis. shirts, where possible exclude personnel from the swing area of the machine Make operators aware, look up and live | 6 | operator |
| 3 | Excavating/ Placing fill | Buried services Striking personnel Overhead services | 1 | Check with authorities, principal contractor and MH before excavating High visibility clothing, movement alarms operational All operators to look up before and during operation | 6 | operator |
| 4 | Lifting Goods and Materials | Lifting equiptment failure Personnel strikes Overhead services/ obstacles | 1 | use only SWL tagged lifting gear/ inspect condition before each use Where possible always remain out of swing area of load, never beneath a load, do not use hand held or tied lanyards to position loads look up and live. | 6 | operator |
| 5 | Loading Trucks/Bins | Striking truck/bin Burying personnel | 1 | maintain eye contact with driver/operator where possible. When loading blind, inspect bins before loading. | 6 | operator |
| 6 | Managing fill stockpile | Uneven surfaces/ trips and falls – low | 4 | Plan to stockpile materials in allotted positions. Maintain in such a way as to prevent creation of unnecessary uneven surfaces in areas of work | 6 | operator |

| ITEMS REQUIRED FOR THIS WORK ACTIVITY |
| --- |
| QUALIFICATIONS | Operator ticket, Green Card |
| TRAINING |  |
| CODES OF PRACTICE OR AS/NZS STANDARDS TO BE COMPLIED WITH | COP Excavation; COP Moving plants on construction sites |

| Declaration by contractors and workers I have been consulted and have assisted in the development of this SWMS. I have been given the opportunity to comment on the content of this SWMS. I have read and understand how I am to carry out the activities listed in this SWMS. I have been supplied with the personal protective equipment identified on this SWMS and I have been given training in the safe use of this equipment. I have read and understand the requirements set out in the material safety data sheets for the hazardous substances identified in this SWMS. |
| --- |
| SWMS 2: EXCAVATOR OPERATION CUT/FILL/TRENCHING |
| NAME | SIGNATURE | DATE |
| Steve |  |  |
| Rob Hanepen |  |  |
| Troy Hanepen |  |  |
| Matt Howell |  |  |