| OHS FORM 05: SAFE WORK METHOD STATEMENT (SWMS) –03 STEEL FIXING |
| --- |
| Company name: Collective Civil Pty Ltd ABN: 53 097 428 003 | This SWMS has been developed and authorised by: |
|  | Name | Kiri Krishnapillai |
|  | Position | Project Manager | Date | 04/05/09 |
|  | Signature |  | Phone |  |
|  |  |  | Mobile | 0458 180 902 |
| DESCRIPTION OF WORK ACTIVITY: STEEL FIXING |
| Trades involved with undertaking this work activity: |
| This SWMS is submitted to (principal contractor): |
| COMPANY: EWG |
| CONTACT NAME: Rodney Swil | CONTACT NAME: |
| SITE ADDRESS: Clarkes Point Hunters Hill | PROJECT DESCRIPTION: Stormwater Treatment and Reuse Clarkes Point Hunters Hill |
| This SWMS was reviewed by (principal contractor): |
| NAME: Rodney Swil | POSITION: Superintendent |
| SIGNATURE: | DATE: |
| PHONE NUMBER: | MOBILE NUMBER: 0419 259 854 |
| Person responsible for supervising and implementing, on the contractor’s behalf, the OHS controls associated with each step of this work activity. |
| NAME: Troy Hanepen POSITION: |
| SIGNATURE: | DATE: 04/05/09 |
| PHONE NUMBER: | MOBILE NUMBER: 0412 992 957 |
| List plant, equipment and tools to be used | List hazardous substances to be used or handled | MSDS available? (Tick) | List PPE to be used | (Tick) | List hazards to consider | (Tick) |
| eg Electric generator | eg Unleaded petrol |  | Hard hat |  | Fall from ladder |  |
|  |  |  | Safety boots |  | Fall from heights |  |
|  |  |  | High-visy clothing |  | Fall from scaffold |  |
|  |  |  | Gloves |  | Contact with electricity |  |
|  |  |  | Hearing protection |  | Falling objects |  |
|  |  |  | Safety glasses |  | Collapse |  |
|  |  |  | UV cream |  | Slip, trips and falls |  |
|  |  |  | Dust masks |  | Manual handing |  |
|  |  |  | 30+ sunscreen |  | Exposure to noise |  |
|  |  |  | Other (specify): |  | Struck by moving plant |  |
|  |  |  |  |  | Inhalation of dust or fumes |  |
|  |  |  |  |  | Cuts |  |
|  |  |  |  |  | Other (specify): |  |
| RISK TABLE How likely is it to be serious? NOTE: If a hazard is rated 1, 2 or 3, take action immediately. What damage could it cause? Very likely (could happen anytime) Likely (could happen sometimes) Unlikely (could happen, but only rarely) Very unlikely (could happen, but probably never will) Death or permanent disability 1 1 2 3 Long term illness or serious injury 1 2 3 4 Medical attention and several days off work 2 3 4 5 First aid needed 3 4 5 6 | How to complete the following form List the step-by-step sequence of tasks required to carry out a work activity from start to finish. List the potential hazards associated with each step, and the related OHS risks. Using the risk table, rate the identified risks. List what controls you will implement to reduce the risks to the lowest possible level. Rate the level of risk once those controls have been implemented (must be 4-6 before you can start work). List the names or positions of the persons responsible for ensuring that the controls are implemented. A separate SWMS is required for each work activity. |

| STEP | Activity step Break the activity down into steps. List the steps in this column. | Hazards Identification Identify any potential hazards associated with each step – and any related risks. Detail the hazards and risks in this column, and enter the risk rating in the next column. | Initial risk rating (1-6) | Controls Implemented Decide what controls to use to eliminate or minimise the risks. Detail the controls in this column, and enter the revised risk rating in the next column. Note: If the risk rating is still 1-3, do not begin work. | Revised risk rating (1-6) | Person responsible |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Transporting reo to worksite | Load falls, back injury from lifting Medium | 2 | Do not overload trucks Take the same precautions for securing the load as you would take on a public road | 6 | Site Manager |
| 2 | Assembly and tie reinforcement | Trip hazard - low Manual handling injuries – high Cuts from wire – medium | 4 | Level job surrounds, remove obstacles Two man lifts,use excavator when able wear Gloves | 6 | Site Manager |
| 3 | Lift reinforcement into place | Cuts from wire – medium Load crushing – medium Load falling | 4 | wear Gloves Check chains are tagged and tested Use tag lines when moving loads long distance. Keep eye contact with operator | 6 | Site Manager |
| 4 | Trimming reinforcement with angle grinder | Electrocution-medium Eye Injury - high Fire - low | 1 | Tag all power tools Inspect for faults at each use Wear full face protection Do not direct sparks at people or flammable substance | 6 | Site Manager |
| 5 | Place caps on the starter bars and duct tape on so they do not fall off easily | Trip hazard - low Manual handling injuries – high | 2 | Gloves, Do not reach out too far to place caps on bars | 6 | Site Manager |

| ITEMS REQUIRED FOR THIS WORK ACTIVITY |
| --- |
| QUALIFICATIONS | Green Card |
| TRAINING | Steel Fixing |
| CODES OF PRACTICE OR AS/NZS STANDARDS TO BE COMPLIED WITH | COP Excavation; COP Moving plants on construction sites |

| Declaration by contractors and workers I have been consulted and have assisted in the development of this SWMS. I have been given the opportunity to comment on the content of this SWMS. I have read and understand how I am to carry out the activities listed in this SWMS. I have been supplied with the personal protective equipment identified on this SWMS and I have been given training in the safe use of this equipment. I have read and understand the requirements set out in the material safety data sheets for the hazardous substances identified in this SWMS. |
| --- |
| NAME | SIGNATURE | DATE |
| Steve |  |  |
| Rob Hanepen |  |  |
| Troy Hanepen |  |  |
| Matt Howell |  |  |