| OHS FORM 05: SAFE WORK METHOD STATEMENT (SWMS) –04 Concreting on Ground |
| --- |
| Company name: Collective Civil Pty Ltd ABN: 53 097 428 003 | This SWMS has been developed and authorised by: |
|  | Name | Kiri Krishnapillai |
|  | Position | Project Manager | Date | 04/05/09 |
|  | Signature |  | Phone |  |
|  |  |  | Mobile | 0458 180 902 |
| DESCRIPTION OF WORK ACTIVITY: Concreting on Ground |
| Trades involved with undertaking this work activity: |
| This SWMS is submitted to (principal contractor): |
| COMPANY: EWG |
| CONTACT NAME: Rodney Swil | CONTACT NAME: |
| SITE ADDRESS: Clarkes Point Hunters Hill | PROJECT DESCRIPTION: Stormwater Treatment and Reuse Clarkes Point Hunters Hill |
| This SWMS was reviewed by (principal contractor): |
| NAME: Rodney Swil | POSITION: Superintendent |
| SIGNATURE: | DATE: |
| PHONE NUMBER: | MOBILE NUMBER: 0419 259 854 |
| Person responsible for supervising and implementing, on the contractor’s behalf, the OHS controls associated with each step of this work activity. |
| NAME: Troy Hanepen POSITION: |
| SIGNATURE: | DATE: 04/05/09 |
| PHONE NUMBER: | MOBILE NUMBER: 0412 992 957 |
| List plant, equipment and tools to be used | List hazardous substances to be used or handled | MSDS available? (Tick) | List PPE to be used | (Tick) | List hazards to consider | (Tick) |
| eg Electric generator | eg Unleaded petrol |  | Hard hat |  | Fall from ladder |  |
|  |  |  | Safety boots |  | Fall from heights |  |
|  |  |  | High-visy clothing |  | Fall from scaffold |  |
|  |  |  | Gloves |  | Contact with electricity |  |
|  |  |  | Hearing protection |  | Falling objects |  |
|  |  |  | Safety glasses |  | Collapse |  |
|  |  |  | UV cream |  | Slip, trips and falls |  |
|  |  |  | Dust masks |  | Manual handing |  |
|  |  |  | 30+ sunscreen |  | Exposure to noise |  |
|  |  |  | Other (specify): |  | Struck by moving plant |  |
|  |  |  |  |  | Inhalation of dust or fumes |  |
|  |  |  |  |  | Cuts |  |
|  |  |  |  |  | Other (specify): |  |
| RISK TABLE How likely is it to be serious? NOTE: If a hazard is rated 1, 2 or 3, take action immediately. What damage could it cause? Very likely (could happen anytime) Likely (could happen sometimes) Unlikely (could happen, but only rarely) Very unlikely (could happen, but probably never will) Death or permanent disability 1 1 2 3 Long term illness or serious injury 1 2 3 4 Medical attention and several days off work 2 3 4 5 First aid needed 3 4 5 6 | How to complete the following form List the step-by-step sequence of tasks required to carry out a work activity from start to finish. List the potential hazards associated with each step, and the related OHS risks. Using the risk table, rate the identified risks. List what controls you will implement to reduce the risks to the lowest possible level. Rate the level of risk once those controls have been implemented (must be 4-6 before you can start work). List the names or positions of the persons responsible for ensuring that the controls are implemented. A separate SWMS is required for each work activity. |

| STEP | Activity step Break the activity down into steps. List the steps in this column. | Hazards Identification Identify any potential hazards associated with each step – and any related risks. Detail the hazards and risks in this column, and enter the risk rating in the next column. | Initial risk rating (1-6) | Controls Implemented Decide what controls to use to eliminate or minimise the risks. Detail the controls in this column, and enter the revised risk rating in the next column. Note: If the risk rating is still 1-3, do not begin work. | Revised risk rating (1-6) | Person responsible |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Back up truck to pour concrete to form or pump | Reverse to damage structures or life | 1 | Make sure driver is aware of the hazards make him get out of the truck and walk the site to be taken. Make sure people are out of the way. | 6 | Site Manager |
| 2 | Attach chutes to deliver concrete | Pinch body parts back strain reverse to damage structure or life | 4 | Wear gloves Attach chutes away from excavation or form and then quide truck to back up with chutes attached and raised to height miss any obstacles. One labour to hold chute and one other labour to guide truck driver. | 6 | Site Manager |
| 3 | Deliver concrete to hopper or excavator bucket | Splash concrete to damage eyes and skin | 4 | Wear Gloves Wear eye protection | 6 | Site Manager |
| 4 | Concrete pump operation | Hose has unexpected blockage and blow out | 2 | Subcontract pump hire personnel must have SWMS signed off. Item specific to point hose away from personnel if freeing a blockage | 6 | Site Manager |
| 5 | Alternate pour concrete to form using excavator | Splash concrete Full bucket may be too heavy for excavator at full reach. May cause excavator to topple Excavator too close to edge of excavation will cause bank to collapse | 2 | Wear Gloves, and safety glasses lower bucket so concrete does not drop more than allowable to segregate and splash. Do not overfill bucket Do not reach out too far to place concrete | 6 | Site Manager |
| 6 | Vibrate concrete to forms | Lifting injury for vibrator Hand injury while vibrating | 4 | Use two people to lift vibrator in position Wear gloves while vibrating | 6 | Site Manager |
| 7 | Shovel and screed concrete to place | Manual lifting and strain injury | 2 | Correct positioning when shovelling and screed do not over stretch | 6 | Site Manager |
| 8 | .Clean up of equipment and tools. | Contamination of waterways or storm water pick-ups. – medium | 4 | All equipment must be washed down in the designated area located in the main site compound. | 6 | Site Manager |

| ITEMS REQUIRED FOR THIS WORK ACTIVITY |
| --- |
| QUALIFICATIONS | Green Card |
| TRAINING | Concreting |
| CODES OF PRACTICE OR AS/NZS STANDARDS TO BE COMPLIED WITH | COP Excavation; COP Moving plants on construction sites |

| Declaration by contractors and workers I have been consulted and have assisted in the development of this SWMS. I have been given the opportunity to comment on the content of this SWMS. I have read and understand how I am to carry out the activities listed in this SWMS. I have been supplied with the personal protective equipment identified on this SWMS and I have been given training in the safe use of this equipment. I have read and understand the requirements set out in the material safety data sheets for the hazardous substances identified in this SWMS. |
| --- |
| SWMS4: Concreting on Ground |
| NAME | SIGNATURE | DATE |
| Steve |  |  |
| Rob Hanepen |  |  |
| Troy Hanepen |  |  |
| Matt Howell |  |  |
| Danny |  |  |
| Kenny |  |  |