| OHS FORM 05: SAFE WORK METHOD STATEMENT (SWMS) –05 Pit Installation |
| --- |
| Company name: Collective Civil Pty Ltd ABN: 53 097 428 003 | This SWMS has been developed and authorised by: |
|  | Name | Kiri Krishnapillai |
|  | Position | Project Manager | Date | 06/09/10 |
|  | Signature |  | Phone |  |
|  |  |  | Mobile | 0458 180 902 |
| DESCRIPTION OF WORK ACTIVITY: Pit Installation |
| Trades involved with undertaking this work activity: |
| This SWMS is submitted to (principal contractor): |
| COMPANY: AUBURN COUNCIL |
| CONTACT NAME: Siva SIVAKUMAR | CONTACT NAME: |
| SITE ADDRESS: STATION ROAD AUBURN | PROJECT DESCRIPTION: Drainage & Road Works |
| This SWMS was reviewed by (principal contractor): |
| NAME: | POSITION: Superintendent |
| SIGNATURE: | DATE: |
| PHONE NUMBER: | MOBILE NUMBER: |
| Person responsible for supervising and implementing, on the contractor’s behalf, the OHS controls associated with each step of this work activity. |
| NAME: Troy Hanepen POSITION: |
| SIGNATURE: | DATE: 06/09/10 |
| PHONE NUMBER: | MOBILE NUMBER: 0412 992 957 |
| List plant, equipment and tools to be used | List hazardous substances to be used or handled | MSDS available? (Tick) | List PPE to be used | (Tick) | List hazards to consider | (Tick) |
| eg Electric generator | eg Unleaded petrol |  | Hard hat |  | Fall from ladder |  |
|  |  |  | Safety boots |  | Fall from heights |  |
|  |  |  | High-visy clothing |  | Fall from scaffold |  |
|  |  |  | Gloves |  | Contact with electricity |  |
|  |  |  | Hearing protection |  | Falling objects |  |
|  |  |  | Safety glasses |  | Collapse |  |
|  |  |  | UV cream |  | Slip, trips and falls |  |
|  |  |  | Dust masks |  | Manual handing |  |
|  |  |  | 30+ sunscreen |  | Exposure to noise |  |
|  |  |  | Other (specify): |  | Struck by moving plant |  |
|  |  |  |  |  | Inhalation of dust or fumes |  |
|  |  |  |  |  | Cuts |  |
|  |  |  |  |  | Other (specify): |  |
| RISK TABLE How likely is it to be serious? NOTE: If a hazard is rated 1, 2 or 3, take action immediately. What damage could it cause? Very likely (could happen anytime) Likely (could happen sometimes) Unlikely (could happen, but only rarely) Very unlikely (could happen, but probably never will) Death or permanent disability 1 1 2 3 Long term illness or serious injury 1 2 3 4 Medical attention and several days off work 2 3 4 5 First aid needed 3 4 5 6 | How to complete the following form List the step-by-step sequence of tasks required to carry out a work activity from start to finish. List the potential hazards associated with each step, and the related OHS risks. Using the risk table, rate the identified risks. List what controls you will implement to reduce the risks to the lowest possible level. Rate the level of risk once those controls have been implemented (must be 4-6 before you can start work). List the names or positions of the persons responsible for ensuring that the controls are implemented. A separate SWMS is required for each work activity. |

| STEP | Activity step Break the activity down into steps. List the steps in this column. | Hazards Identification Identify any potential hazards associated with each step – and any related risks. Detail the hazards and risks in this column, and enter the risk rating in the next column. | Initial risk rating (1-6) | Controls Implemented Decide what controls to use to eliminate or minimise the risks. Detail the controls in this column, and enter the revised risk rating in the next column. Note: If the risk rating is still 1-3, do not begin work. | Revised risk rating (1-6) | Person responsible |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Excavating/ Placing fill | Buried services Striking personnel Overhead services | 1 | Check with authorities, principal contractor and MH before excavating Dial before you dig High visibility clothing, movement alarms operational All operators to look up before and during operation | 6 | Site Manager |
| 2 | Excavation more than 1.5m deep must be shored or benched | Trench or hole collapse Falls | 1 | Erect shoring in accordance with Australian standards or proprietary shoring drag box Fence off excavations and provide safe access in and out of excavation | 6 | Site Manager |
| 3 | Provide bedding for precast pit | Gas in trenches Trench collapse | 1 | Provide ventilation and gas detection equipment if there is any consideration of enclosed or confined space Do not venture away from unsupported trenches | 6 | Site Manager |
| 4 | Lift & place precast unit in place. | Falls Load falls | 2 | Do not stand on pit edges without harness support or providing a ladder or form board across trench Check lifting equipment is certified and adequate and indate | 6 | Site Manager |
| 5 | Backfill & Compact around pit | Work near moving plant Falls | 2 | Good operator worker coordination | 6 | Site Manager |

| ITEMS REQUIRED FOR THIS WORK ACTIVITY |
| --- |
| QUALIFICATIONS | Green Card |
| TRAINING |  |
| CODES OF PRACTICE OR AS/NZS STANDARDS TO BE COMPLIED WITH | COP Excavation; COP Moving plants on construction sites |

| Declaration by contractors and workers I have been consulted and have assisted in the development of this SWMS. I have been given the opportunity to comment on the content of this SWMS. I have read and understand how I am to carry out the activities listed in this SWMS. I have been supplied with the personal protective equipment identified on this SWMS and I have been given training in the safe use of this equipment. I have read and understand the requirements set out in the material safety data sheets for the hazardous substances identified in this SWMS. |
| --- |
| NAME | SIGNATURE | DATE |