|  |  | Legislation/Codes of Practice |
| --- | --- | --- |
| SWMS-08 |  | OH&S Act 2000, OH&S Regulation 2001, Excavation Work (WorkCover Code of Practice), Moving Plant on Construction Sites (WorkCover Safety Guide). |
| TRAFFIC CONTROL |  | Training required to complete work |
|  |  | All persons are to be inducted into this SWMS. All Traffic Controllers to have RTA accredited ticket for Stop/Slow Bat. |
|  |  | Personnel & Qualifications |
|  |  | All operators of machinery are to have WorkCover accredited tickets. |
|  |  | Inspection/ Maintenance on Plant/Equipment before use |
| PERSON RESPONSIBLE FOR SWMS IMPLEMENTATION |  | All Traffic Controllers to have required PPE: Broad brimmed hat, tinted safety glasses, Traffic Controller Safety Vest, Safety Boots, high visibility clothing. |
|  |  | Risk Rating Matrix Table |
| Name | Position |  | Critical – C 1 - 3 High – H 4 - 10 Moderate – M 11 - 15 Low – L 16 -25 |
|  | Project Manager |  |  |
|  | Site Manager |  | Severity of Consequences |
|  |  | Could kill, permanently disable or cause very serious damage. Could cause serious injury (major LTI) or major damage. Could cause typical LTI / MTC or moderate damage. Could cause 1st Aid injury or minor damage Couldn’t cause injury or damage |
| Issue No | Issue Date | Amendments/Remarks |  |  |
|  |  |  |  | Probability of Happening |
|  |  |  |  | A – ALMOST CERTAIN to happen B – LIKELY to happen at some point C – MODERATE – possible, it might happen D – UNLIKELY, not likely to happen E – RARE, practically impossible |

Approved:														Date:

| Induction Record. This Safe Work Method Statement has been shown and explained to me. I understand these procedures and I agree to abide by them. |
| --- |
| Inductors Initials: | Name: | Signature: | Date: | Inductors Initials: | Name: | Signature: | Date: |

| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Note: All persons who perform Traffic Controller duties must be free from the effects of Alcohol, or any substance that may cause drowsiness or lack of concentration. |
| 1 | Set up traffic controls and operate. (Same controls required for removal) | Controller hit by a vehicle. | C | 1 | 4 | Warning signs erected. Use only RTA accredited Traffic Controllers. Traffic Controller is to be visible to oncoming traffic. Approach speed of vehicles to be restricted <60 km/h Traffic Controller is to stand to the side. Workers to wear highly visible clothing & all appropriate PPE. Ensure there is an escape route planned. Use approved Traffic Control Plan | D | 1 | 7 | Site Manager, All Workers |
| 2 | Work adjacent to traffic. | Worker being hit by a passing vehicle. | C | 1 | 4 | Workers to wear highly visible clothing & all appropriate PPE. Approach speed of vehicles to be restricted <60 km/h Traffic Controllers to be relieved after 2 hours work for a minimum 15 minutes before returning | D | 1 | 7 | Site Manager, All Workers |
|  |  | Pedestrian being hit by Plant. | C | 2 | 8 | Use approved Traffic Control Plan Delineate traffic path with hats. | D | 2 | 12 | Site Manager |
|  |  | Public vehicle being hit by Plant. | C | 2 | 8 | Use approved Traffic Control Plan Erect 15km/hr speed signs. Traffic Controllers are to maintain a line of sight. Traffic Controllers are to use hand signals & ‘stop/go’ bats. | D | 2 | 12 | Site Manager |
| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| 3 | Communication | Traffic Controllers cannot see each other | C | 1 | 4 | Additional Traffic Controllers to be utilised; or Provide portable 2-way radios | D | 1 | 7 | Site Manager, All Workers |
| 4 | Night Work | Poor visibility | B | 1 | 2 | Wear white overalls with reflective tape Use lighted red hand-held wand to supplement STOP/SLOW bat Locate Traffic Controller at a spot on the road that is lit Use 2-way radio control | D | 1 | 7 | Site Manager |