|  |  | Legislation/Codes of Practice |
| --- | --- | --- |
| SWMS-09 |  | OH&S Act 2000, OH&S Regulation 2001, Excavation Work (WorkCover Code of Practice), Moving Plant on Construction Sites (WorkCover Safety Guide). |
| WORKING AT HEIGHTS |  | Training required to complete work |
|  |  | All persons are to be inducted into this SWMS, with any special training requirements identified prior to this induction. |
|  |  | Personnel & Qualifications |
|  |  | All operators of machinery are to have WorkCover accredited tickets. |
|  |  | Inspection/ Maintenance on Plant/Equipment before use |
| PERSON RESPONSIBLE FOR SWMS IMPLEMENTATION |  | All plant is to be inspected by the operator on a daily basis using Robson’s Daily Plant Inspection Checklist. |
|  |  | Risk Rating Matrix Table |
| Name | Position |  | Critical – C 1 - 3 High – H 4 - 10 Moderate – M 11 - 15 Low – L 16 -25 |
|  | Project Manager |  |  |
|  | Site Manager |  | Severity of Consequences |
|  |  | Could kill, permanently disable or cause very serious damage. Could cause serious injury (major LTI) or major damage. Could cause typical LTI / MTC or moderate damage. Could cause 1st Aid injury or minor damage Couldn’t cause injury or damage |
| Issue No | Issue Date | Amendments/Remarks |  |  |
|  |  |  |  | Probability of Happening |
|  |  |  |  | A – ALMOST CERTAIN to happen B – LIKELY to happen at some point C – MODERATE – possible, it might happen D – UNLIKELY, not likely to happen E – RARE, practically impossible |

Approved:														Date:

| Induction Record. This Safe Work Method Statement has been shown and explained to me. I understand these procedures and I agree to abide by them. |
| --- |
| Inductors Initials: | Name: | Signature: | Date: | Inductors Initials: | Name: | Signature: | Date: |

| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Securing Tensar material to batter for stabilisation | Angle of batter exceeding 15 degrees with risk of slipping/falling further than 2 metres | C | 2 | 8 | Fall arrest system to be used | D | 2 | 12 | Site Manager |
|  |  | Where working within 2 metres of an edge that would expose worker to a free fall greater than 2 metres | C | 2 | 8 | Fall protection must be put in place | D | 2 | 12 | Site Manager |
|  |  | Type of surface worked on e.g. rock or soil/clay Slip/trip hazards may be caused by vegetation on batter, loose material, noticeable deterioration of surface, wet surface Hazards posed by type of access provided | C | 2 | 8 | Consideration to installation of permanent/semi permanent fall protection facilities, such as installation of permanent anchorage points for attaching a fall arrest system On batters with an incline/decline >45 degrees, provision of elevated work platform should be considered If a tree is chosen as suitable anchorage point for fall protection, steps must be taken to protect tree against damage (ringbarking) by rope or sling Persons using rope access must be competent in its use If hand tools are used, they must be attached/secured to prevent falling on those who may be working below | D | 2 | 12 | Site Manager |
| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |