|  |  | Legislation/Codes of Practice |
| --- | --- | --- |
| SWMS 11 |  | OH&S Act 2000, OH&S Regulation 2001, Excavation Work (WorkCover Code of Practice), Moving Plant on Construction Sites (WorkCover Safety Guide). |
| Hazardous Materials |  | Training required to complete work |
|  |  | All persons are to be inducted into this SWMS, with any special training requirements identified prior to this induction. |
|  |  | Personnel & Qualifications |
|  |  | All operators of machinery are to have WorkCover accredited tickets. |
|  |  | Inspection/ Maintenance on Plant/Equipment before use |
| PERSON RESPONSIBLE FOR SWMS IMPLEMENTATION |  | All plant is to be inspected by the operator on a daily basis using Robson’s Daily Plant Inspection Checklist. |
|  |  | Risk Rating Matrix Table |
| Name | Position |  | Critical – C 1 - 3 High – H 4 - 10 Moderate – M 11 - 15 Low – L 16 -25 |
|  | Project Manager |  |  |
|  | Site Manager |  | Severity of Consequences |
|  |  | Could kill, permanently disable or cause very serious damage. Could cause serious injury (major LTI) or major damage. Could cause typical LTI / MTC or moderate damage. Could cause 1st Aid injury or minor damage Couldn’t cause injury or damage |
| Issue No | Issue Date | Amendments/Remarks |  |  |
|  |  |  |  | Probability of Happening |
|  |  |  |  | A – ALMOST CERTAIN to happen B – LIKELY to happen at some point C – MODERATE – possible, it might happen D – UNLIKELY, not likely to happen E – RARE, practically impossible |

Approved:														Date:

| Induction Record. This Safe Work Method Statement has been shown and explained to me. I understand these procedures and I agree to abide by them. |
| --- |
| Inductors Initials: | Name: | Signature: | Date: | Inductors Initials: | Name: | Signature: | Date: |

| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Delivery & storage | Contact with chemicals due to packaging being damaged. | C | 2 | 8 | All hazardous substances to be delivered in unopened and undamaged packaging. All hazardous substances are to be stored and handled in accordance with the MSDS. No hazardous substances are to be stored in the site shed. | D | 2 | 12 | Site Manager |
| 2 | Use | Contact with chemicals due to incorrect handling procedure. | C | 2 | 8 | Personnel to be trained in use of hazardous substances. | D | 2 | 12 | Site Manager |
|  |  | Lack of information. | C | 3 | 13 | Review MSDS and assess risk. | D | 3 | 17 | Site Manager, All Workers |
|  |  | Not wearing correct PPE. | C | 2 | 8 | Use PPE as described on MSDS. | D | 2 | 12 | Site Manager, All Workers |
|  |  | Elevated exposure level. | C | 2 | 8 | Provide mechanical ventilation. All personnel to be provided with appropriate PPE as per MSDS. | D | 2 | 12 | Site Manager |

| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |